## Slide 1: Optimal Traffic Light Signaling Based on Genetic Algorithm Approach
By: G5
Alok Yadav 58090001
Tan Tianyu 58090005
Sajeerat Aussavaruengsuwat 58090036
Advisor: Dr. Chaiwat Nuthong

## Slide 2: Overview
Introduction
Literature Review
Problem description
Objectives
Proposed solution
Experiment
Research plan
Conclusion

## Slide 3: Introduction

## Slide 4: Introduction
Traffic congestions are a recurring problem that has plagued humanity for decades.
Objective: Use genetic algorithms to alter traffic light signal timings, in order to optimize the flow of traffic

## Slide 5: Literature Review

## Slide 6: Literature review
[1] P. Gora, “A genetic algorithm approach to optimization of vehicular traffic in cities by means of configuring traffic signals”, in “Emergent Intelligent Technologies in the Industry”, 2011, pp. 1-10, ISBN: 978-3-642-22731-8.
[2] P. Gora and P. W. Pardel, "Application of Genetic Algorithms and High-Performance Computing to the Traffic Signal Setting Problem", 2015.

## Slide 7: Literature review
Traditional approach to optimizing traffic signals:
  Create a population of genotypes where each gene represents a crossroad
  Use a traffic simulation model to evaluate the fitness of the genotypes
  Use genetic algorithm to progressively get better traffic signal timings
Notes: Pang:::

## Slide 8: Results
Results were measured in terms of total waiting time
Results varied depending on model used
Using the Traffic Simulation Framework gave improvements between 3% and 6%

## Slide 9: Problem Description

## Slide 10: Problem description
Prior research only uses current traffic conditions to optimize traffic
Optimization period is quite short (5-10 min)
Optimizing traffic over longer periods of time is challenging due to high time complexity of the simulations.
Notes: Use real time traffic condition to analyze & it could optimized the period only 5-10 minutes ahead.
Since it analyzed according to current traffic data so optimizing over long time might be challenging because each optimization takes time.

## Slide 11: Objectives

## Slide 12: Objectives
Approximate traffic variations in a selected area on a day-to-day basis
Implement a traffic simulation model
Implement a genetic algorithm based solution to improve total waiting time by 8% in simulated traffic from current setting to modified setting

## Slide 13: Proposed Solution

## Slide 14: Novelty
Optimization will be done on sequences of traffic signals over long periods of time (>= 1 hr)
Figure 3: sequence of timings for a 3
crossroad network in our proposed method
Figure 2: timings for a 3 crossroad
network in prior research

## Slide 15: Proposed solution
Select an area which shows recurring traffic congestions.
Obtain traffic data covering the congestion period on multiple days and average it.
Use a genetic algorithm (GA1) to optimize traffic over the congestion period using our novelty.

## Slide 16: Proposed solution
From the signal timings obtained, save the following
  Traffic densities at each road over the congestion period corresponding to the best solution from GA1
  The best genotypes from the last population

## Slide 17: Proposed solution
For future congestions, use another genetic algorithm (GA2) that optimizes traffic at small time intervals using the following:
  Solutions obtained from GA1 to generate new solutions
  A fitness function that tries to alter the current traffic densities to mimic traffic densities obtained from GA1
Notes: For future congestions in the same area at the same time, use another genetic algorithm (GA2) that optimizes traffic in real time based on the following criteria

## Slide 18: Proposed solution
Figure 4: Proposed solution
Click to add text

## Slide 19: Benefits of proposed method
Formulates a control strategy based on historic traffic data
Optimizing sequences of traffic signals over longer period gives better improvement in traffic conditions
Benefits of longer period simulations without running them in GA2

## Slide 20: Research goals
Goal 1: Ascertain the degree of variability in traffic conditions for the selected region during the selected time interval.
Goal 2: Measure the improvement in traffic conditions when using GA1 to optimize traffic.
Goal 3: Measure the improvement in traffic conditions when using GA2 to optimize traffic.

## Slide 21: Experiments

## Slide 22: Experiments
Experiment objective: measure the ability of GA1 to optimize traffic
Only 6 experiments have been conducted thus far, due to the computational limitations
Only 3 of them show significant convergence

## Slide 23: Experiment setup
Implement GA1 using DEAP, GA1 is run locally (ASUS ROG G751 JT)
Integrate GA1 with TSF (run remotely on virtual machine in azure cloud)
Set parameters for GA1 (described in next slides)
Run GA1

## Slide 24: Experiments
 | 1st Experiment | 2nd Experiment | 3rd Experiment
Time duration | 20 min | 20 min | 20 min
Time step duration | 2 min | 2 min | 2 min
Num. Generation | 10 | 5 | 15
Num. Individual | 20 | 40 | 50
Mutation | Flip bit (0.05) | Flip index (0.1) | Flip index (0.1)

## Slide 25: Experiment results
Experiment 1: 8.27% improvement
Experiment 2: 7.60% improvement
Experiment 3: 13.21% improvement

## Slide 26: Research plan

## Slide 27: Current progress
Goal 1:
  Implemented scripts to obtain travel speed information from TomTom API
  Implemented scripts to extract relevant information from travel speed data

## Slide 28: Current progress
Goal 2:
  Implemented GA1 using DEAP module in python
  Integrated Traffic Simulation Framework (TSF) with GA1 to test fitness of generated solutions
  Performed small scale experiments

## Slide 29: Current progress
Goal 3:
  Implemented GA2 using DEAP module in python
  Integrated Traffic Simulation Framework (TSF) with GA2 to test fitness of generated solutions

## Slide 30: Future work
Goal 1:
  Select region, time interval and gather required data
  Alter simulations based on acquired data
Goal 2-3:
  Alter the implementation to run on computationally competent hardware
  Use grid search to set the GA parameters
  Conduct further experiments corresponding to goal 3
  Implement a graphical interface for visualization

## Slide 31: Conclusion

## Slide 32: Conclusion
Optimizing sequences of traffic signals seems to be a better way of optimizing traffic; however, further research needs to be conducted, in order to make our approach computationally feasible.